## Slide 1: LAB - 07
陳培殷老師
國立成功大學 資訊工程系

## Slide 2
Sequential Circuit (1/3)
A sequential circuit is a system whose outputs at any time are determined from the present combination of inputs and the previous inputs or outputs.
Combinational
Logic Circuit
..
..
n input
variables
m output
variables
Memory
Elements
states
Sequential components contain memory elements
The output values of sequential components depend on the input values and the values stored in the memory elements

## Slide 3
Sequential Circuit (2/3)
正緣同步電路
低位準非同步重置

## Slide 4
Sequential Circuit (3/3)
Blocking statement vs nonblocking statement

## Slide 5: Lab I (1/3)
請設計一個具備下列功能的計數器：
  正緣同步電路，低位準非同步重置
  當reset訊號為0，將目前狀態暫停，輸出維持0
  當reset訊號為1
    Up_Down = 0 ，每秒計數減1
      EX：0 -> F -> E -> …… -> 2 -> 1 -> 0 -> F ……
    Up_Down = 1 ，每秒計數加1
      EX：0 -> 1 -> 2 -> …… -> E -> F -> 0 -> 1 ……
  FPGA版之clock頻率為50MHz，需藉由除頻器將clock訊號降為1Hz
    實現方式為透過一個計數器，計算經過幾個時脈正緣，當計數到50 × 106 即代表經過一秒
Notes: 可解釋為overflow

## Slide 6: Lab I (2/3)
請將計數的數值顯示於七段顯示器
系統架構圖請參考下方
  Input ：clock(CLOCK_50) , reset(SW0), Up_Down(SW1)
  Output ：out(7 bits，HEX06~HEX00)
可使用structural description設計，其中，除頻器及計數模組為循序電路，七段顯示器控制模組則為組合電路

## Slide 7: Lab I (3/3)
輸出範例
Up_Down = 0
reset
…
Up_Down = 1
reset
…

## Slide 8: Lab - Hint(1/2)
Frequency Divider (sequential circuit)
  將clock頻率從50MHz降為1Hz
Counter (sequential circuit)
  每秒進行計數
Seven Display (combinational circuit)
  將Counter數值轉為七段顯示器控制訊號
Module呼叫範例 (Structural description)
  FrequencyDivider u_FreqDiv (.clk(clock), .reset(reset), .clk_div(clock_div));
  Counter u_counter(.clk(clock_div), .reset(reset), .count(count));
  SevenDisplay u_display(.count(count), .out(out));
module_name unit_name(.port_name(signal_name),.port_name(signal_name)……)

## Slide 9: Lab – Hint(2/2)
除頻器範例：
  每0.5秒改變一次訊號(div_clk)
低位準同步reset

## Slide 10
Notice
請勿命名中文或數字開頭的資料夾
Device family 請確認與 FPGA Chip 符合 (5CEFA4F23C7)
Top module name & Project name 需要一致
在組合電路中，case、if…else…若沒有寫滿，合成後會產生latch