## Slide 1: LAB - 10
陳培殷老師
國立成功大學 資訊工程系

## Slide 2: Traffic Light System
請設計一紅綠燈系統電路(變化順序: 綠 -> 黃 -> 紅)
電路腳位
  Input: clock(CLOCK_50)、reset(reset button)
  Output: dot_row(8 bits)、dot_col(8 bits)、out(7 bits)
使用七段顯示器根據燈號進行倒數(16進制)
  綠燈: 15數到0
  黃燈: 5數到0
  紅燈: 10數到0
Reset按鈕控制:
  將系統設為初始狀態：燈號為綠燈，顯示綠燈圖像，計數器設為15
綠燈
黃燈
紅燈
Notes: 做不太完，可以考慮先不做點矩陣

## Slide 3: Hint
使用兩個除頻器
  一個用於計數及state切換 (1Hz)
  一個用於點矩陣顯示 (10000Hz)
在state machine加入條件判斷，當計數為0時切換state
The example for dot matrix control

## Slide 4: LED Dot Matrix Display (1/3)
In DE0-CV external board
column
row[7]
row[6]
row[5]
row[4]
row[3]
row[2]
row[1]
row[0]
[7][6][5][4][3][2][1][0]
DM1
DM0
[7][6][5][4][3][2][1][0]

## Slide 5: LED Dot Matrix Display (2/3)
The dot matrix is controlled by 8 column lines and 8 row lines.
When the signal of column is 1 and the signal of row is 0, the dot will be turned on.
0 0 1 0 0 0 0 0
1 1 1 0 1 1 1 1
Row Line
Column Line
Dot Matrix
Your Design
module …(…);
output [7:0]col;
output [7:0]row;
.
.
.
.
.
……
……
LED
row[4] = 0
column[5] = 1

## Slide 6
Scan the rows in turns frequently and control the column lines according to the row in operation, thus the image will be shown due to Persistence of vision.
0 0 0 1 1 0 0 0
0 1 1 1 1 1 1 1
0 0 1 0 0 1 0 0
1 0 1 1 1 1 1 1
0 1 0 0 0 0 1 0
1 1 0 1 1 1 1 1
1 1 0 0 0 0 1 1
1 1 1 0 1 1 1 1
→
→
→
→ …
=>
LED Dot Matrix Display (3/3)
  Clock must be as 10000 Hz for display !!!
Step 1
Step 2
Step 3
Step 4

## Slide 7
Notice
請勿命名中文或數字開頭的資料夾
Device family 請確認與 FPGA Chip 符合 (5CEFA4F23C7)
Top module name & Project name 需要一致
在組合電路中，case、if…else…若沒有寫滿，合成後會產生latch